## Slide 1: FleetWise: The Fleet Management System
A Smart Vehicle Monitoring and Predictive Analytics Solution
College Project Presentation

## Slide 2: Project Overview
FleetWise is a comprehensive fleet management system designed for real-time vehicle tracking, driver behavior analysis, emission monitoring, and predictive maintenance. The system is split into three main components: Frontend, Backend, and Hardware.

## Slide 3: Problem Statement
Managing a fleet of vehicles involves tracking vehicle location, monitoring driver behavior, ensuring timely maintenance, and complying with emission norms. Manual systems are inefficient, costly, and prone to human error.

## Slide 4: Objectives
- Enable real-time vehicle tracking via a web dashboard
- Predict vehicle maintenance requirements using ML
- Monitor driver behavior and environmental pollution
- Build a scalable system using modern web technologies

## Slide 5: System Architecture
1. Sensor data from GPS, MPU9250, MQ135, and OBD-II is collected using Arduino Uno WiFi R3.
2. Data is transmitted via HTTP to a PHP backend hosted on XAMPP.
3. The React + Vite frontend fetches data to display in real-time.
4. Machine Learning models process data for maintenance, pollution, and driver analytics.

## Slide 6: Frontend: React + Vite + Material UI
- Built using React for modular UI development
- Vite ensures fast bundling and hot module replacement
- Material UI provides a responsive and modern look
- Real-time charts and vehicle cards for tracking

## Slide 7: Backend: XAMPP + PHP
- XAMPP stack used for local server hosting
- PHP scripts receive sensor data via HTTP POST
- Stores data in MySQL database for frontend & ML access
- FastAPI used for serving ML predictions to frontend

## Slide 8: Hardware Components
- Arduino Uno WiFi R3 (ESP8266 integrated)
- NEO-6M GPS module for location data
- MPU9250 for acceleration and orientation
- MQ135 for air pollution (PPM level)
- OBD-II Bluetooth for vehicle diagnostics

## Slide 9: Machine Learning Modules
- Predictive Maintenance: Analyzes OBD and sensor data
- Pollution Emission: Detects high emission vehicles
- Driver Behavior: Detects harsh braking, acceleration

## Slide 10: Real-time Web Dashboard
- Visualizes data from multiple vehicles
- Location maps, emission charts, alerts
- Live updates from backend database
- ML analysis shown with predictions

## Slide 11: Results and Highlights
- Successfully tracked multiple vehicles in real time
- Detected pollution threshold breaches
- Predicted maintenance with 85% accuracy
- Detected harsh driving behavior patterns

## Slide 12: Conclusion & Future Scope
- FleetWise provides an integrated solution for fleet monitoring
- Future improvements:
• GSM fallback for areas with no WiFi
• Mobile app version
• More robust ML models with larger datasets